## Slide 1
Making Biosolids Disappear –
The Magic Of Hydrothermal Liquefaction
Michael Washer – Director of The Merrick Consultancy
Presented to: International Biomass Conference & Expo 2018
April 18, 2018
www.merrick.com

## Slide 2
Process Overview

## Slide 3
Chemical Reactions

## Slide 4
A Brief History Of Hydrothermal Liquefaction
1920’s
2007
2010 to Present
1970’s
1990’s
Concept of HTL proposed. First patent in 1925
OPEC Embargo sparks interest in alternative liquid fuels. Multiple R&D projects, including Shell Oil
PNNL picks up the baton. Developed complementary Catalytic Hydrothermal Gasification process.
RFS II drives development of renewable fuel technologies
Explosion of interest in HTL development and commercialization.

## Slide 5
Waste Biomass Feedstocks

## Slide 6
HTL Process Schematic

## Slide 7
Catalytic Hydrothermal Gasification Process Schematic

## Slide 8
Carbon conversion in CHG ≈ 80%
Phosphorous recovery ≈ 99%
Biosolids processed up to 20wt%
1
2
3
4
5
Carbon conversion in HTL ≈ 50%
PROCESS
PERFORMANCE
Energy efficiency > 85%

## Slide 9
Double the energy recovery of pyrolysis
Bio-gas is siloxane and H2S free
Footprint is < 50% that of anaerobic digester
1
2
3
4
5
No feed drying
HTL & CHG
ADVANTAGES
GHG reduction 3X that of anaerobic digester
6
Modular system, fabricated off-site
7
Process is robust and non-biological

## Slide 10
HPPS Project
Converts 2 wet tons per day of 20wt% algae into biocrude
Designed, built, and commissioned by Merrick
1
2

## Slide 11
Next Step – The HYPOWERS Project
Hydrothermal Processing Of Wastewater Solids
Capacity of 15 wet tons per day of biosolids (equivalent to a wastewater plant serving around 45,000 people)
1
2
Located at the Central San Plant, in Martinez, CA
3
Project is a consortium, including WRF, Merrick, Genifuel, PNNL, Central San & others
4
Cost share, with matching funding from BETO
5
Project will demonstrate all aspects of the HTL and CHG technologies
6

## Slide 12
Heat Integration
Nutrient Recycle To Fertilizer
Biocrude Post Treating
1
2
3
4
5
6
Capital Cost Reduction
Standardization
Modularization
Scale-up
Low Cost Components
PATH TO COMMERCIALIZATION
Bio-Gas Post Treating
Business Model Development

## Slide 13
Thankyou
Questions ?
Michael Washer – Director of The Merrick Consultancy
303 353 3875
michael.washer@Merrick.com
www.merrick.com